A little Christmas tree (wood made)

Here is the list of materials used and the process followed to create the Christmas tree.

MATERIALS

N° 3 battens  of fir tree 15 x 0.8 x 2000 mm - to make the branches
N° 2 battens of fir tree 20 x 0.8 x 2000 mm - to make the branches
N° 1 batten of fir tree 30 x 0.8 x 2000 mm - to make the branches
N° 1 batten of fir tree 60 x 30 x 500 mm - to make the base
N° 1 x 130 mm – 40 mm diameter of Piece of circular fir tree - to make the trunk

N° 1 threaded rod of 1 meter, diameter 6 mm, washers and nuts

PROCESS

- 3 battens 15 x 0.8 x 2.000 mm were cut in :

N°  4 pieces x 40 mm
N°  4 pieces x 60 mm
N°  5 pieces x 80 mm
N° 12 pieces x 180mm
N° 10 pieces x 120mm
N° 13 pieces x 140 mm

-  2 battens 20 x 0.8 x 2.000 mm were cut in :

N°   8 pieces x 250 mm
N° 10 pieces x 200 mm

- 1 batten of fir tree 30 x 0.8 x 2.000 mm was cut into 6 pieces of 330 mm

All the pieces obtained were rounded with a grinder and drilled (6 mm) at one end. I have shaped the battens (spear point!) with the plane, file and sandpaper. The little cylindrical piece representing the trunk of the tree, I have shaped it slightly conical with a plane and sandpaper and I drilled in the center for its entire length.

the cross base made with special joints between wood battens of larger section, it was drilled to fix the threaded rod on which, starting from the trunk of the tree, I have assembled all the branches (from the longest to end up with smaller ones).

All the branches have been positioned in a circular and distributed mode and whit a washer and a nut on the top of threaded rod, I pulled all the pieces together. On top of the tree I inserted a cylindrical piece of wood to cover the threaded rod. After that it will be covered by the old golden tip.

At this point, the work is finish. You can decorate the tree as you prefer. We have decided to paint the tree with a white opaque water paint so the decorations (usually red) can stand out better.

This type of construction allows you to "grow" your tree. Is enough to extend the threaded rod and increase the number and length of the branches starting from the trunk. If the number of branches to be added will be consistent, it will be necessary to replaced the threaded bar with a larger cross section (8 - 10 mm) to allow the tree to stay perpendicular right!

... GOOD JOB AND MY BEST WISHES TO ALL !!

www.ricicreare.it – info@ricicreare.it

# Text boxes

Firenze, 8 Dicembre 2015

www.ricicreare.it